## Slide 1
DEPARTMENT OF ELECTRONICS & COMMUNICATION ENGINEERING
Design and Simulation of an
Automatic Street Light Control System
A Major Project Report
Submitted by KATUKURI SAI KAUSHIK — 2620040013 PINNAMANENI MOKSHA SRI — 2620040034 K VINAY — 2620040050
SAI CHARAN VEDULA-2620040062
Institution KLH BACHUPALLY Academic Year- 2026–2027

## Slide 2
01 · INTRODUCTION
Introduction
Street lighting is one of the largest continuous electricity loads for any municipality, typically running on fixed timers regardless of actual traffic, ambient light, or weather. An Automatic Street Light Control System uses sensing and embedded control to switch lights ON only when ambient darkness demands it, and OFF (or dimmed) when daylight or motion conditions allow — cutting waste without cutting safety. This project falls within the domain of Embedded Systems and Automation, combining sensor electronics, microcontroller-based logic, and power switching to build an energy-efficient, low-maintenance lighting solution suited for smart-city infrastructure.
Energy Efficiency
Lights operate only when needed, reducing grid load and wasted power.
Smart Infrastructure
A building block for smart-city and IoT-enabled municipal systems.
Low Maintenance
Automatic operation removes dependence on manual switching.
Automatic Street Light Control System
2

## Slide 3
02 · PROBLEM STATEMENT
Problem Statement
Conventional street lighting relies on fixed timers or manual switching, operating at full brightness through the entire night irrespective of real ambient light levels or road usage.
Key Limitations of the Existing Approach
Energy Wastage
Lights stay on during moonlit nights, early dawn, or when no vehicles/pedestrians are present.
Manual Dependency
Human-operated switching is inconsistent, delayed, and prone to error.
No Adaptability
Fixed timers cannot adjust to seasonal changes in sunrise/sunset or weather-driven darkness.
High Maintenance Cost
Frequent bulb failure from continuous full-brightness operation increases upkeep.
Automatic Street Light Control System
3

## Slide 4
03 · OBJECTIVES
Objectives
Specific, measurable goals guiding the design and simulation of the system.
Automate Light Switching
Design a circuit that switches street lights ON/OFF automatically based on ambient light intensity.
Reduce Energy Consumption
Minimize unnecessary power usage compared to fixed-timer lighting.
Sensor-Based Detection
Use a Light Dependent Resistor (LDR) to accurately sense day/night transitions.
Microcontroller Control Logic
Implement decision logic on a microcontroller for reliable, programmable switching.
Simulate & Validate
Simulate the circuit to verify correct switching behaviour before hardware deployment.
Analyze Performance
Evaluate output results, response time, and potential energy savings.
Automatic Street Light Control System
4

## Slide 5
04 · LITERATURE SURVEY
Literature Survey / Existing System
Approach | Description | Limitation
Timer-Based Switching | Lights turn ON/OFF at fixed pre-set clock times each day. | Cannot adapt to seasonal or weather-based daylight changes.
Manual Grid Switching | Utility staff manually operate switches at substations. | Labour-intensive, slow response, human error.
Photocell Relay Systems | A photoresistor relay toggles power at a fixed light threshold. | No intelligence, dimming, or fault reporting; single fixed threshold.
Basic LDR + Relay Circuits | Analog LDR circuit directly drives a relay to switch the lamp. | No microcontroller logic, no scheduling flexibility, prone to false triggers from noise.
Gap identified: Existing solutions lack sensor + microcontroller integration with simulated validation — the motivation for the proposed system.
Automatic Street Light Control System
5

## Slide 6
05 · PROPOSED SYSTEM
Proposed System
The proposed system integrates an LDR sensor with a microcontroller-based control unit to automatically drive the street light through a relay/driver stage — enabling intelligent, threshold-based, and (optionally) dimmable operation.
Real-Time Light Sensing
LDR continuously monitors ambient light and feeds analog data to the controller.
Microcontroller Decision Logic
Programmable threshold comparison replaces rigid, fixed-timer switching.
Efficient Power Switching
Relay/driver stage switches load cleanly, minimizing switching losses.
Optional Motion Sensing
PIR input can further dim/brighten lights based on road activity.
Simulated Validation
Behaviour verified in simulation (e.g., Proteus) before hardware build.
Improved Energy Efficiency
Reduces wasted operating hours versus timer-based existing systems.
Automatic Street Light Control System
6

## Slide 7
06 · SYSTEM ARCHITECTURE
System Architecture / Block Diagram
Power Supply
Unit
5V/12V Regulated
LDR Sensor
Light Intensity
Signal
Conditioning
Comparator / ADC
Microcontroller
Decision Logic
Relay / Driver
Circuit
Switching Stage
Street Light
(LED/Lamp)
Output Load
Power Supply Bus
Signal / Control Flow: Ambient light → LDR sensing → Conditioning → Microcontroller logic → Relay switching → Street light output
Closed-loop behaviour: the microcontroller continuously polls the LDR reading, so the light state automatically tracks changing ambient conditions in real time — no manual intervention required.
Automatic Street Light Control System
7

## Slide 8
07 · METHODOLOGY
Methodology / Implementation
1
Component Selection
Choose LDR, microcontroller (e.g., Arduino/8051), relay module, resistors, and LED/lamp load.
2
Circuit Design
Design the LDR voltage-divider sensing stage and interface it to the controller's analog/digital input.
3
Logic Programming
Program the threshold-comparison logic to trigger the relay when darkness is detected.
4
Simulation
Build and run the circuit in simulation software (e.g., Proteus) to verify switching behaviour.
5
Testing & Validation
Vary simulated light levels to confirm correct ON/OFF response and record results.
Key Circuit Components
LDR (Light Dependent Resistor) — sensing element
Microcontroller (e.g., Arduino / 8051 / PIC) — control logic
Voltage divider resistor — sets sensing bias
Comparator (op-amp, e.g., LM358) — threshold detection
Relay module / MOSFET driver — power switching
LED / lamp — output load representing the street light
Regulated power supply — 5V/12V system power
Working Principle: while the LDR resistance is low (daylight), the divider output keeps the controller input above threshold and the relay stays open. As darkness increases LDR resistance, the input crosses threshold and the controller energizes the relay to switch the light ON.
Automatic Street Light Control System
8

## Slide 9
08 · RESULTS & DISCUSSION
Results and Discussion
Truth Table — LDR vs. Street Light State
Ambient Light | LDR Resistance | Controller Input | Light Output
Bright (Day) | Low | HIGH | OFF
Dim (Dusk) | Rising | Near Threshold | OFF → ON transition
Dark (Night) | High | LOW | ON
Simulation Output
[Insert Proteus / simulation screenshot here showing the circuit in day-state (light OFF) and night-state (light ON)]
Discussion
• The simulated circuit correctly switched the load ON as the LDR crossed the pre-set darkness threshold, and OFF as light levels rose. • Response was near-instantaneous in simulation, with no false triggering under stable lighting. • Results confirm the design meets the stated objectives of automatic, threshold-based control.
~30–40%
Est. energy saving
vs. fixed-timer operation
< 1s
Simulated switching
response time
Figures are illustrative — replace with values recorded from your own simulation runs.
Automatic Street Light Control System
9

## Slide 10
CIRCUIT DIAGRAM

## Slide 11
09 · CONCLUSION
Conclusion
The project successfully designed and simulated an Automatic Street Light Control System that replaces inefficient fixed-timer lighting with intelligent, sensor-driven, microcontroller-based switching.
All Objectives Met
Automated switching, sensor integration, and simulated validation were each achieved as planned.
Demonstrated Efficiency
Simulation results show reduced unnecessary operating hours versus timer-based systems.
Scalable Foundation
The design can be extended with motion sensing, dimming, and IoT connectivity for future smart-city deployment.
Thank You